## Slide 1
Trainium architecture, generation by generation
Green tags: added in that generation
Trainium
Trn1 | NeuronCore-v2
HBM 32 GiB
NC-v2
NC-v2
NeuronLink-v2
6 CC-Cores
4 engines per core
GPSIMD custom ops
Dynamic shapes
Stochastic rounding
trn1.32xlarge
16-chip 2D torus
Trainium2
Trn2 | NeuronCore-v3
24 GB
24 GB
24 GB
24 GB
NC-v3
NC-v3
NC-v3
NC-v3
NC-v3
NC-v3
NC-v3
NC-v3
NeuronLink-v3
16 CC-Cores
8 cores per chip
Logical NeuronCore
Structured sparsity
cFP8 exponent bias
16-chip torus
64 / UltraServer
Trainium3
Trn3 | NeuronCore-v4
HBM 144 GiB
NC-v4
NC-v4
NC-v4
NC-v4
NC-v4
NC-v4
NC-v4
NC-v4
NeuronLink-v4
16 CC-Cores
MXFP8 / MXFP4
Near-memory accumulation
Fast exp on Vector
NeuronSwitch-v1
SW
UltraServer
Gen1: 64 chips
Gen2: 144 chips

## Slide 2
Logical NeuronCore (LNC) on Trainium2
8 physical cores per chip
LNC = 1
HBM 24 GB
NC
v3
NC
v3
NC_v3
NC_v3
HBM 24 GB
NC
v3
NC
v3
NC_v3
NC_v3
HBM 24 GB
NC
v3
NC
v3
NC_v3
NC_v3
HBM 24 GB
NC
v3
NC
v3
NC_v3
NC_v3
8 logical cores per chip
trn2.48xlarge: 128 cores
LNC = 2 (default)
HBM 24 GB
NC
v3
NC
v3
NC_v3d
HBM 24 GB
NC
v3
NC
v3
NC_v3d
HBM 24 GB
NC
v3
NC
v3
NC_v3d
HBM 24 GB
NC
v3
NC
v3
NC_v3d
4 logical cores per chip
trn2.48xlarge: 64 cores
Runtime setting = Compiler setting

## Slide 3
Near-memory accumulation on NeuronCore-v4
Adding incoming B into A in SRAM
Generic: copy, then add
Source
B
DMA
SRAM
B (copy)
A
Engine: A + B
1
2
2
3
NeuronCore-v4
Source
B
DMA
SRAM
A ← A + B
1
read-add-write
in one transfer