## Slide 1
vLLM stays as is; the model plugs into the plugin
Grey: vLLM. Blue: Neuron plugin. Green: you write it (nemotron_h)
vLLM
OpenAI API server
request management
KV block management
Neuron plugin
scheduler: prefill and decode apart
ModelRunner: graphs to NEFF
KV cache allocation
nemotron_h
5 contract methods
Mamba state pool
4 NKI kernels
The only change outside nemotron_h: 2 lines in registry.py

## Slide 2
Five methods the ModelRunner calls
Green: you write it. Blue: the plugin does the rest
Method
You write
Plugin does
from_configs
read the HF config and max_num_seqs
build the model, one graph per bucket
load_weights
TP sharding, experts stored per expert
read the checkpoint shards
get_kv_spec
declare the 6 attention layers only
size the KV blocks from free memory
bind_kv_cache
attach KV to the attention layers
allocate the KV cache
forward
dispatch each layer by its type
trace and run every step
Mamba state is not KV: it lives in a model-side pool, one row per request

## Slide 3
52 layers of three kinds: Mamba2 and MoE rewritten for Trainium
Green: Mamba2. Yellow: MoE. Blue: attention. Every rewrite is pinned by a CPU test
Mamba2 x 23
sequential scan does not compile
128-token chunks as matmuls
state carried across segments
padding masked out of the state
MoE x 23
128 experts, top-6 + 1 shared
router: compares and sums only
no data-dependent gather
decode reads 6 experts only
Attention x 6
no rotary position embedding
the only layers with KV
GQA, 32 query / 2 KV heads
existing plugin kernels

## Slide 4
Decode: 72.5 ms to 9.0 ms per token
One request, TP=4 on one Trainium2 chip. Grey: start. Green: helped. Dim: no gain
start: all 128 experts
72.5 ms
read only the 6 experts
14.0 ms
topk, then index the weights
attention without KV copies
12.8 ms
GQA, graphs per context length
MoE decode NKI kernel
12.6 ms
almost no gain
Mamba2 decode NKI kernel
10.0 ms
conv + SSM + norm in one kernel
matvec NKI kernel
9.0 ms
projections: x fixed, weights streamed
With concurrent requests supported, the final build decodes one request in 9.2 ms

## Slide 5
Four NKI kernels: split work over 2 cores, batch the DMAs
Green: kernel. Each splits across the 2 physical cores of a logical core with no exchange
Mamba2 decode
one SSM group per core
all requests in one DMA per tile
SSD prefill
one SSM group per core
exponents from clamped differences
MoE decode
intermediate axis split in 2
experts fetched by index
matvec
output columns split in 2
x stationary, weights streamed
Prefill: about 800 to 2,600 tokens/s with the SSD kernel

## Slide 6
Concurrent requests: find the state row by the first KV block
Blue: decode batch from the plugin. Green: state pool in the model
decode batch: rows reorder every step
state pool: 2N + 1 rows
row 0
request B, first block 41
row 1
request A, first block 7
row 2
padding
row 0
owner 7: A
row 1
owner 41: B
...
free
last
scratch for padding
Lookup uses only compares and max: one compiled graph serves every step
8 concurrent requests: 216 tokens/s in total (one request alone: 91 to 94). A request's output is identical whatever shares its batch